## Slide 1
Phase I Final Presentation:
Safety Analysis For Evaluating (SAFE) sUAS
NASA SBIR Contract Number: NNX16CL88P
Presented to: Rania Ghatas, NASA LaRC
IAI | Ankit Tyagi (PI) Sri Ayyalasomayajula Nikhil Nigam Fred Wieland
Purdue | Prof. Inseok Hwang Chiyu Zhang
December 02, 2016

## Slide 2: Presentation Outline
Schedule
Problem Description
Phase I Tasks
Phase I Highlights
Detailed Technical Discussion
Phase II Plans
Questions/Action Items and Wrap Up

## Slide 3: Project Schedule
Tasks\Months | 1 | 2 | 3 | 4 | 5 | 6
Task 1 |  |  |  |  |  | 
Task 2 |  |  |  |  |  | 
Task 3 |  |  |  |  |  | 
Task 4 |  |  |  |  |  | 
Task 5 |  |  |  |  |  | 
Task 6 |  |  |  |  |  | 
Task 7 |  |  |  |  |  | 
06/10
07/10
08/10
09/10
10/10
11/10
12/10
Today

## Slide 4: PROBLEM DESCRIPTION
What is the problem? How will SAFE sUAS help?

## Slide 5: Problem and Proposed Solution
No standard safety tool for sUASs exists today
Safety procedures for sUAS will require ability to simulate sUAS trajectories with high level of precision
SAFE sUAS Approach
  Develop medium fidelity sUAS trajectory model informed by high fidelity simulations and flight test for variety of sUASs
  Use these models as inputs to existing UAS safety models
Small UAS in the NAS OV1 (UTM Project)
“Currently, there is no established infrastructure to enable and safely manage the widespread use of low-altitude airspace and UAS operations, regardless of the type of UAS”
Ref: https://utm.arc.nasa.gov/index.shtml

## Slide 6: Phase I Work Plan
Task 1: Hold kickoff meeting and establish program requirements
Task 2: Setup 6-DOF flight dynamics and control simulation
Task 3: Use 6-DOF closed-loop flight simulation for generation of sUAS performance files
Task 4: Modify KTG for sUAS trajectory generation using performance files from Task 3
Task 5: Validate modified-KTG trajectories against 6-DOF simulation
Task 6: Demonstrate prototype simulation analysis results for sUAS
Task 7: Develop concepts for Phase II and transition
Additional Tasks Executed
High fidelity battery drain modeling
Hardware in the loop testing for battery drain rate

## Slide 7: Phase I Highlights
Developed a scalable sUAS trajectory modeling architecture that allows for integrating high fidelity performance data with medium fidelity trajectory models
Developed trajectory generator for rotorcraft sUAS and validated the results using high fidelity 6-DOF simulations
Developed high fidelity battery drain rate model validated by hardware in the loop tests
Performed preliminary safety analysis for package delivery and aerial imaging missions using sUAS

## Slide 8: Technical Overview

## Slide 9: sUAS Trajectory Generator (sUTG) Overview
UAS Flight Demand
  Flight plan-like information for each sUAS flight
  Sample flight plans were developed for this briefing
Rotorcraft Performance Database (RPD)
  Aircraft performance under different mission segment and altitude combinations
sUAS Trajectory Generator (sUTG)
  3 DOF trajectory model that computes flight trajectories at 500 millisecond interval

## Slide 10: RPD Development
6-DOF Model
  Quadcopter model developed to mimic IRIS implemented in jMAVSim
6-DOF Mission Simulations
  Refinement Loop: To develop the 6-DOF model
  Production Loop: To populate RPD

## Slide 11: SAFE sUAS Workflow
Kinematic Trajectory Generator
sUTG
Testbed
Rotorcraft Performance Database
Safety
Analyses
Quadcopter Design
Rotorcraft Performance Database Requirements
sUTG and Performance
Database Refinement Loop
Refinement Loop
Validated
6-DOF Model
6-DOF Model
sUAS Simulations | HIL | Flight Tests*
*Phase II Plans

## Slide 12: Detailed technical discussion
Development of sUTG and use of RPD

## Slide 13: sUTG Architecture
The architecture is similar to Kinematic Trajectory Generator
  Well known, industry vetted, trajectory model for fixed wing large aircraft
  Uses EUROCONTOL’s BADA file for performance computations
sUTG comprises of three main modules:
  Navigation Control Module
    Computes desired speed, heading and ROCD
  Low level control
    Computes desired acceleration and turn rate
  Plant
    Uses equations of motion to update sUAS state
Goal: Use as much of KTG’s algorithms as possible to develop sUTG
Result:
sUTG = KTG for quadcopter sUAS

## Slide 14: sUTG: Equations of Motion
KTG is a 3-DOF model and therefore allows us to re-use much of the existing modules to simulate small quadcopter flights
States
  Latitude ( Le)
  Longitude (λe)
  Altitude (h)
  TAS (V)
  Vertical speed (vz)
  Heading (ξ)
  Mass (m)
Control Inputs
  Longitudinal acceleration (a)
  Vertical acceleration (az)
  Commanded turn rate ( )
  Fuel consumption rate (η)
where,
Vw: wind speed
Existing equations of motion modeled in KTG

## Slide 15: sUTG: Low Level Controller
The Low level controller calculates:
  Acceleration in longitudinal direction
  Acceleration in vertical direction
  Turn rate
The low level controller required the following modifications to account for the sUAS performance limitations:
  PI controller associated with each control loop
    Re-tuned gains for sUAS
  Saturator limits accelerations and turn rate
    Defined appropriate limits for sUAS
  Saturator limits speeds
    Defined appropriate limits for sUAS

## Slide 16: Rotorcraft Performance Database
RPD serves as lookup table for the 3-DOF sUAS Trajectory Generator (sUTG) model and is populated by operating the 6-DOF model (from Purdue) over a set of procedures.
The structure and use is inspired by EUROCONTROL’s Base of Aircraft Data (BADA) files
RPD specify cruise, climb, descent, and hover performance at different flight levels, throttle settings and other aircraft state parameters. More flight modes can be added in the future.

## Slide 17: Use of RPD

## Slide 18: Detailed technical discussion
Development of 6-DOF Model and RPD

## Slide 19: Overview
6-DOF flight dynamics modeling and simulation platform development for RPD creation and validation of sUTG
  6-DOF high-fidelity dynamics modeling
    6-DOF modeling parameters
    Software interface
  Simulation platform development
    Hardware in-the-loop (HIL) simulation setup
    Integrate battery drain database
  HIL Simulation
    Generate the Rotorcraft Performance Database (RPD)

## Slide 20: Overview
VTOL sUAS Considered
Name | IRIS+ | 
Vendor | 3D Robotics | 
Type | VTOL | 
Weight (lbs.) | 3 | 
Endurance (min.) | 16-22 | 
Number of motors | 4 | 

## Slide 21: 6-DOF Quadcopter Dynamics
6-DOF Equations of Motion:
Thrust and Torque Equations:
IRIS+ coordinate frames
Top view of IRIS+

## Slide 22: 6-DOF Quadcopter Modeling
Modeling parameters:
  System parameters
    Mass
    Moments of inertia
    Positions of the rotors
    Maximum rotor thrust and torque
    Propeller aerodynamic coefficients
Obtaining parameter values
  mass, moments of inertia, and thrust arms: by measurement
  thrust and rotor drag factors: from manual
  maximum thrust and torque: by experiment
    the maximum thrust is obtained from experiment
    the maximum torque is calculated from the test output
Rotor Testbed

## Slide 23: 6-DOF Model Software Interface
jMAVSim flight simulator (open source)
  Multi-rotor dynamics simulator
  Suitable for both hardware- and software-in-the-loop purposes
  Builds customized quadcopter models from user-defined parameters
6-DOF Modeling
  Set the modeling parameters in the source code
  A user manual is developed to provide the details

## Slide 24: Simulation Platform
HIL Simulation Components (All open source):
  jMAVSim: dynamic simulator
  Qgroundcontrol (QGC): ground control station
  PX4: autopilot software
  Pixhawk: autopilot hardware
QGC
jMAVSim
Pixhawk

## Slide 25: Simulation Inputs/Outputs
Inputs: waypoints by mouse clicking/input files/user interface
  quadcopter’s status: e.g. takeoff, landing, etc.
  coordinate: latitude, longitude, alt
  for quadcopters: hovering time
Outputs: data files containing variable names and values
  a list of over 120 variables including: speed, attitude, position, etc.
  select the desired output from the list
Select the outputs
Mission planning (waypoints)
right figure: operation window
Notes: id: the quadcopter will first move to WP 1, and then to WP 2, and so on;
param2: that if the sphere with this radius is hit by the quadcopter, the WP counts as reached;
param3: set to 0 if the quadcopter is desired to pass through the WP; otherwise this parameter controls the radius to fly by the WP, where a positive value for a clockwise orbit and a negative value for a counter-clockwise orbit;

## Slide 26: Battery Drain Rate Modeling
Motivation:
  The battery drain rate (mAh/s) changes during flight
  Analogy with ‘fuel consumption’
  Essential for performance and safety analysis
Objective:
  Integrate a battery drain rate database
  Challenge: NO battery models available among the quadcopter community
Proposed approach: battery test
  Test the battery performance at different battery/thrust levels
  Build a lookup table of battery drain rate
  Find the corresponding battery drain rate according to simulation output

## Slide 27: Battery Modeling
Test setup:
  Fix the quadcopter to a heavy plate to prevent flight
  Use a remote radio controller to control thrust
  Record the thrust output and battery info in QGC
  Battery specs:
    capacity = 2200mAh
    voltage = 11.1V
Quadcopter fixed here
Battery
Thrust controller

## Slide 28: Battery Modeling
Test procedure
  For low thrust level testing, let the battery deplete at a constant thrust
  For high thrust level testing, vary throttle settings and note the changing thrust values
Raw data:
  Time in ms
  Thrust as percentage of the maximum
  Energy consumed from the start in mAh
Battery level:
Drain rate: mAh/s

## Slide 29: Battery Modeling
Drain rate table
Battery level: 40%~80%, at steps of 5%
  40% battery: safety threshold from experiment
  80% battery: nominal battery level
Thrust level: 55%~90%, at steps of 1%
  55% thrust: hover thrust
  90% thrust: safety upper bound in autopilot
  table entry: drain rate (mAh/s)
Table shows battery drain rate under combinations of battery level and thrust levels

## Slide 30: Rotorcraft Performance Database (RPD)
RPD file
  Performance data at nominal (80%) and critical (40%) battery levels
  Four basic flight modes: cruise, climb, descend, and hover
  Create simulation scenarios corresponding to the flight modes
  Simulation output: groundspeed, altitude, climb rate, thrust
  Use the thrust output to find the corresponding battery drain rate from the drain rate table
  Use the data to populate RPD table
Flight mode | Simulation scenario
Cruise | Cruise at nominal speed at a given altitude
Climb | Takeoff to 400 ft. AGL
Descend | Land from 400 ft. AGL
Hover | Hover at a given altitude

## Slide 31: sUAS Performance Data for IRIS (.RPD)
Speed limits for flight modes
Baseline levels of battery
Battery drain rate for a given flight mode, battery level, altitude and TAS
TAS at different flight levels and battery conditions

## Slide 32: Validation
Compare sUTG with 6-DOF model for conformance

## Slide 33: Flight Simulation 1 (High Cruise)
Flight plan
  Origin: KGAI (Montgomery County Airpark, Gaithersburg, MD  NW of DC)
  Destination: about 1.7 km to southeast of KGAI
  Cruise altitude: 300 ft. AGL
  Aircraft: IRIS
  Cruise speed: 6.7 m/s
  Flight duration: ~9 min.
  Hover:
    Altitude: 300 ft. AGL
    Duration: 3 min.

## Slide 34: Results
Hover
TO
CR
HV
CR
DS/LD
Battery Vs. Time
Distance Vs. Time

## Slide 35: Validation using 6-DOF Model
sUTG follows the flight plan well except waypoint 3
sUTG is designed to treat close waypoints as “fly-by” rather than “fly-over”
sUTG initially overshoots the cruise altitude by 25 feet
Result of low level controller gains
Deviation in total flight time is due to “fly-over” waypoint
Latitude (deg.)
Longitude (deg.)
Some deviations with the climb and descent rate
Good overall conformance over the entire mission

## Slide 36: Flight Simulation 2 (Short Flight)
Flight plan
  Origin: a generic suburban area
  Destination: about 0.5 km to east of origin
  Cruise altitude: 80 ft. AGL
  Aircraft: IRIS
  Cruise speed: 6.7 m/s
  Hover:
    Duration: 10 seconds
    Altitude: 80 ft. AGL
  Duration: 3 min.

## Slide 37: Validation using 6-DOF Model
Latitude (deg.)
Longitude (deg.)
Ground track deviation due to sUTG’s treatment waypoints leading to acute angles as “fly-by” rather than “fly-over”
sUTG initially overshoots the cruise altitude by 25 feet
Result of low level controller gains
Deviation in total flight time is due to “fly-over” waypoint
Some deviations with the climb and descent rate
Good overall conformance over the entire mission
Overall, sUTG shows good conformance with 6-DOF model for both simulations

## Slide 38: Safety analyses
Fly two sUAS missions, assess Loss of Separation

## Slide 39: sUAS Simulations

## Slide 40: Simulation Setup
100 flights for each application  200 sUAS flights total
Flights simulated during an 8 hr. window  9 AM to 5 PM EST
  Typical business hours of operation
Safety Metric: Potential loss-of-separation (LOS) events
  Assumption: LOS for sUAS is defined as an instance when two sUAS are closer than 50 ft. horizontally or vertically
Total flights | 200
Potential flight pairs | 19,900
Flight pairs airborne at same time | 700
Flight pairs with LOS | 6
LOS location

## Slide 41: Lessons Learned
Modeling performance of each aircraft is necessary for any sUAS operations technology
  Majority of pilots and even some manufacturers are unaware of performance limits
Critical to model battery drain, the UAS performance is closely tied to battery remaining.
  Need battery information for mission planning, contingency management, and performance estimation
Medium fidelity trajectory model informed by high fidelity performance data performs well
  Code is efficient enough to simulate large number of aircraft
  Results show good conformance with high fidelity model

## Slide 42: Phase II Plans
Perform market survey to identify five most popular sUAS and choose five sUAS to model
  Ensure at least one fixed wing, rotorcraft and hybrid sUAS is chosen.
Develop performance tables for selected sUAS
Enhance UTG to account for impact of winds and gusts
Enhance UTG to account for sensor uncertainty
Model the impact of non-standard sUAS configurations
Perform flight tests to validate UTG predictions
Develop sUAS missions around expected operations
Analyze the safety impacts of operating sUAS mission on NAS safety

## Slide 43
For questions or comments
contact
Ankit Tyagi
Mail: atyagi@i-a-i.com